LCLS Undulator Quadrupole Magnet

FIDUCIALIZATION REPORT

| Inspector: | Keith Caban |
| --- | --- |
| Responsible Engineer: | Scott Anderson |
| Date: | Friday, June 13, 2008 |
| Work Order/Charge No.: | 88-1400-5 |
| Serial Number: | SLAC – 000743 / STAMPED – 28 |
| URL of Fiducial Report: | http://www-group.slac.stanford.edu/met/Quality/FIDUCIAL REPORTS/LCLS UNDULATOR QUADS/000743.pdf |

Part Set-up – Coordinate System Set-up

Spatial Alignment

- Geometric axis of the poles of the magnet.

Planar Alignment

- Plane on where Aluminum Base Rests

“Z” Zero

- Mid-plane of the magnet (middle of upstream and downstream ends).

“X” & “Y” Zero

- Geometric axis of the poles of the magnet.

| Front View | Side View |
| --- | --- |

Tooling Ball Measurements/Locations

Top View looking from +Y

Tooling Ball Adapter Cylinder Projected 1” Offset to the Tooling Ball Adapter Plane

| Tooling Ball | FORM | Cyl. Dia. | X | Y | Z | b |
| --- | --- | --- | --- | --- | --- | --- |
| TB 1 | 0.00016 | 0.25003 | 3.37646 | 6.81366 | 1.49258 | 0.00007 |
| TB 2 | 0.00022 | 0.24983 | -3.37125 | 6.81395 | 1.50739 | 0.00010 |
| TB 3 | 0.00020 | 0.24989 | -3.38066 | 6.81482 | -1.49096 | 0.00008 |
| TB 4 | 0.00012 | 0.24999 | 3.37036 | 6.81490 | -1.50750 | 0.00010 |
| TB 5 | 0.00010 | 0.25019 | 6.57565 | 0.14022 | -0.00723 | 0.00013 |

Z-distance of Quad = 3.59320

Pole Tip Additional Data

*Data looking from Downstream End

| Side | Pole Dist A-C | Pole Dist B-D | Gap 1 | Gap 2 | Gap 3 | Gap 4 |
| --- | --- | --- | --- | --- | --- | --- |
| Downstream End (+Z) | 0.43341 | 0.43163 | 0.15854 | 0.15974 | 0.15830 | 0.16001 |
| Upstream End (-Z) | 0.43275 | 0.43312 | 0.15918 | 0.16067 | 0.16103 | 0.15847 |

| Side | A-Rad | B-Rad | C-Rad | D-Rad |
| --- | --- | --- | --- | --- |
| +Z | 0.21594 | 0.21592 | 0.21747 | 0.21571 |
| -Z | 0.21639 | 0.21647 | 0.21636 | 0.21665 |

| Side | J | K | L | M | N | O | P | Q |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| +Z | 0.07780 | 0.08013 | 0.07988 | 0.07811 | 0.08044 | 0.08189 | 0.07785 | 0.08049 |
| -Z | 0.08072 | 0.07869 | 0.07978 | 0.07966 | 0.07952 | 0.08054 | 0.08013 | 0.08031 |

Quadrupole Roll Angle

** Tolerance in milliradians is ± 5

Roll of the Base of Quad to Poles



milliradians

# Text boxes

+Y

+Z

+Y

+X

+Z

TB 5

+X