LCLS Undulator Quadrupole Magnet

FIDUCIALIZATION REPORT

| Inspector: | Keith Caban |
| --- | --- |
| Responsible Engineer: | Scott Anderson |
| Date: | Friday, June 13, 2008 |
| Work Order/Charge No.: | 88-1400-5 |
| Serial Number: | SLAC – 000746 / STAMPED – 27 |
| URL of Fiducial Report: | http://www-group.slac.stanford.edu/met/Quality/FIDUCIAL REPORTS/LCLS UNDULATOR QUADS/000746.pdf |

Part Set-up – Coordinate System Set-up

Spatial Alignment

- Geometric axis of the poles of the magnet.

Planar Alignment

- Plane on where Aluminum Base Rests

“Z” Zero

- Mid-plane of the magnet (middle of upstream and downstream ends).

“X” & “Y” Zero

- Geometric axis of the poles of the magnet.

| Front View | Side View |
| --- | --- |

Tooling Ball Measurements/Locations

Top View looking from +Y

Tooling Ball Adapter Cylinder Projected 1” Offset to the Tooling Ball Adapter Plane

| Tooling Ball | FORM | Cyl. Dia. | X | Y | Z | b |
| --- | --- | --- | --- | --- | --- | --- |
| TB 1 | 0.00015 | 0.25005 | 3.37069 | 6.81342 | 1.50366 | 0.00014 |
| TB 2 | 0.00018 | 0.25000 | -3.38313 | 6.80933 | 1.49044 | 0.00018 |
| TB 3 | 0.00017 | 0.24987 | -3.37567 | 6.81109 | -1.50791 | 0.00009 |
| TB 4 | 0.00017 | 0.25004 | 3.37360 | 6.81334 | -1.49532 | 0.00007 |
| TB 5 | 0.00017 | 0.25006 | 6.57474 | 0.12967 | 0.00712 | 0.00015 |

Z-distance of Quad = 3.59435

Pole Tip Additional Data

*Data looking from Downstream End

| Side | Pole Dist A-C | Pole Dist B-D | Gap 1 | Gap 2 | Gap 3 | Gap 4 |
| --- | --- | --- | --- | --- | --- | --- |
| Downstream End (+Z) | 0.43432 | 0.43154 | 0.15976 | 0.16017 | 0.16075 | 0.15789 |
| Upstream End (-Z) | 0.43277 | 0.43403 | 0.15787 | 0.16035 | 0.15957 | 0.16155 |

| Side | A-Rad | B-Rad | C-Rad | D-Rad |
| --- | --- | --- | --- | --- |
| +Z | 0.21851 | 0.21573 | 0.21582 | 0.21581 |
| -Z | 0.21634 | 0.21775 | 0.21643 | 0.21628 |

| Side | J | K | L | M | N | O | P | Q |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| +Z | 0.08069 | 0.07952 | 0.07837 | 0.08007 | 0.07968 | 0.08161 | 0.07856 | 0.08006 |
| -Z | 0.08099 | 0.07918 | 0.08237 | 0.07838 | 0.07949 | 0.07978 | 0.08057 | 0.07859 |

Quadrupole Roll Angle

** Tolerance in milliradians is ± 5

Roll of the Base of Quad to Poles



milliradians

# Text boxes

+Y

+Z

+Y

+X

+Z

TB 5

+X