LCLS Undulator Quadrupole Magnet

FIDUCIALIZATION REPORT

| Inspector: | Keith Caban |
| --- | --- |
| Responsible Engineer: | Scott Anderson |
| Date: | Friday, June 13, 2008 |
| Work Order/Charge No.: | 88-1400-5 |
| Serial Number: | SLAC – 000747 / STAMPED – 12 |
| URL of Fiducial Report: | http://www-group.slac.stanford.edu/met/Quality/FIDUCIAL REPORTS/LCLS UNDULATOR QUADS/000747.pdf |

Part Set-up – Coordinate System Set-up

Spatial Alignment

- Geometric axis of the poles of the magnet.

Planar Alignment

- Plane on where Aluminum Base Rests

“Z” Zero

- Mid-plane of the magnet (middle of upstream and downstream ends).

“X” & “Y” Zero

- Geometric axis of the poles of the magnet.

| Front View | Side View |
| --- | --- |

Tooling Ball Measurements/Locations

Top View looking from +Y

Tooling Ball Adapter Cylinder Projected 1” Offset to the Tooling Ball Adapter Plane

| Tooling Ball | FORM | Cyl. Dia. | X | Y | Z | b |
| --- | --- | --- | --- | --- | --- | --- |
| TB 1 | 0.00012 | 0.25008 | 3.36703 | 6.81661 | 1.49570 | 0.00012 |
| TB 2 | 0.00012 | 0.25008 | -3.38086 | 6.81450 | 1.48922 | 0.00020 |
| TB 3 | 0.00016 | 0.25013 | -3.37383 | 6.81225 | -1.51397 | 0.00012 |
| TB 4 | 0.00013 | 0.25007 | 3.37379 | 6.81367 | -1.50364 | 0.00007 |
| TB 5 | 0.00020 | 0.25000 | 6.57980 | 0.14359 | -0.00468 | 0.00018 |

Z-distance of Quad = 3.57883

Pole Tip Additional Data

*Data looking from Downstream End

| Side | Pole Dist A-C | Pole Dist B-D | Gap 1 | Gap 2 | Gap 3 | Gap 4 |
| --- | --- | --- | --- | --- | --- | --- |
| Downstream End (+Z) | 0.43934 | 0.43474 | 0.16029 | 0.15782 | 0.16044 | 0.16020 |
| Upstream End (-Z) | 0.43216 | 0.43287 | 0.15680 | 0.16018 | 0.15917 | 0.16083 |

| Side | A-Rad | B-Rad | C-Rad | D-Rad |
| --- | --- | --- | --- | --- |
| +Z | 0.21728 | 0.21741 | 0.22206 | 0.21734 |
| -Z | 0.21614 | 0.21613 | 0.21603 | 0.21675 |

| Side | J | K | L | M | N | O | P | Q |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| +Z | 0.07961 | 0.08149 | 0.07871 | 0.07984 | 0.08045 | 0.08047 | 0.07735 | 0.08083 |
| -Z | 0.07952 | 0.07955 | 0.08128 | 0.07825 | 0.07855 | 0.07996 | 0.08022 | 0.07966 |

Quadrupole Roll Angle

** Tolerance in milliradians is ± 5

Roll of the Base of Quad to Poles



milliradians

# Text boxes

+Y

+Z

+Y

+X

+Z

TB 5

+X