VAC CHMBR, PLS PICK / ATTEN

FIDUCIALIZATION REPORT

| Inspector: | Keith Caban |
| --- | --- |
| Customer: | Marc Campell |
| Date: | Wednesday, November 11, 2009 |
| Work Order/Charge No.: | 9120547 |
| Serial Number: | 001 |
| Drwg. #: | SA-391-900-10 Rev 1 |
| URL of Fiducial Report: | \\Web002\www-group\met\Quality\FIDUCIAL REPORTS\SA-391-900-10\SA-391-900-10 SN 001.pdf |

Part Set-up – Coordinate System Set-up

Used Datums A, B, & C for CSY.

Planar Alignment

- Axis of Port 1 flange to Port 17 flange is the Z axis in which positive Z is pointing towards Port 17.

Spatial Alignment

- Plane of Datum –A-  (Port 3), which points in the positive Y direction.

“Z” Zero

- Plane of Datum –C- (Port 1) which sets zero in Z.

“X” & “Y” Zero

- X, Y zero is the axis created by Port 1 & 17 flanges (see planar alignment)

Tooling Ball Measurements/Locations

Using ½” Diameter Tooling Balls with 1” extension

TB’s are scribed on Part located near TB Holes and/or TB Adapters (welded)

| Tooling Ball | Form | Diameter | X | Y | Z |
| --- | --- | --- | --- | --- | --- |
| TB 1 | 0.00027 | 0.49992 | 4.25791 | 3.30361 | 4.50664 |
| TB 2 | 0.00021 | 0.49655 | -0.00618 | 3.30087 | 0.25995 |
| TB 3 | 0.00022 | 0.50003 | -6.50180 | 3.30599 | 2.02562 |
| TB 4 | 0.00190 | 0.49441 | -6.49424 | 3.30814 | 7.02965 |
| TB 5 | 0.00182 | 0.48940 | -3.91437 | 0.04167 | 18.29950 |
| TB 6 | 0.0240 | 0.49375 | 0.02023 | 3.84614 | 16.02870 |
| TB 7 | 0.00108 | 0.49029 | 3.83553 | 0.02708 | 18.29666 |

Port Locations (Polar distance from centerline (XY) & Z Location

# Text boxes

+Y

+Z