LUSI AMO VACUUM CHAMBER

FIDUCIALIZATION REPORT

| Inspector: | Keith Caban |
| --- | --- |
| Customer: | Jean Charles Castagna |
| ate: | Wednesday, June 09, 2010 |
| Work Order/Charge No.: | 25783-1 |
| Serial Number: | 001 |
| Drwg. #: | SC-391-212-10 Rev 0 |
| URL of Fiducial Report: | \\Web002\www-group\met\Quality\FIDUCIAL REPORTS\SC-391-212-10\SN 001.pdf |

Part Set-up – Coordinate System Set-up

- Axis of Port 1 flange to Port 10 flange is the Z axis in which “positive Z” is pointing towards Port 10.

Spatial Alignment

- Plane of top flange that points and sets the direction in “positive Y”.

“Z” Zero

- The axis of the Bottom and Top Flanges. (2 Circles)

“X” & “Y” Zero

- X, Y zero is the axis created by Port 1 & 10 flanges (see planar alignment)

Tooling Ball Measurements/Locations

Using ½” Diameter Tooling Balls with 1” extension

TB’s are scribed on Part located near TB Holes and/or TB Adapters (welded)

*- Used ½” Diameter Tooling ball with ½” extension due to space. (only on TB 4)

| Tooling Ball | Form | Diameter | X | Y | Z |
| --- | --- | --- | --- | --- | --- |
| TB 1 | 0.00001 | 0.50007 | 0.00573 | 6.95821 | -11.29097 |
| TB 2 | 0.00090 | 0.49914 | -11.26586 | 6.96669 | 0.00058 |
| TB 3 | 0.00002 | 0.50007 | 0.00087 | 6.93617 | 11.26680 |
| TB 4* Used ½” ext. | 0.00023 | 0.49930 | 10.79466 | 6.94029 | -0.00201 |
| TB 5 | 0.00071 | 0.49823 | -11.27902 | -9.29891 | -0.04736 |
| TB 6 | 0.00031 | 0.49960 | 0.13681 | -9.30938 | -11.26757 |
| TB 7 | 0.00006 | 0.50003 | 11.27132 | -9.30935 | 0.05665 |
| TB 8 | 0.00031 | 0.49820 | 12.92856 | 5.48613 | -0.02823 |
| TB 9 | 0.00022 | 0.49906 | 12.96545 | -0.17782 | -5.48037 |
| TB 10 | 0.00018 | 0.49951 | -12.92524 | 4.49787 | 0.03091 |
| TB 11 | 0.00012 | 0.49894 | -12.89611 | -0.17273 | -4.47891 |
| TB 12 | 0.00042 | 0.49915 | -12.91245 | -0.30550 | 4.46723 |

# Text boxes

Port 1

+Y

+Z

Port 10

Bottom Flange

Top Flange