LCLS SXR LE SHUTTER VACUUM CHAMBER ASSY

FIDUCIALIZATION REPORT

| Inspector: | Keith Caban |
| --- | --- |
| Responsible Engineer: | Jim DeLor |
| Date: | Thursday, June 26 2014 |
| Work Order/Charge No.: | 231066-3/20 |
| Serial Number: | 86668310-1 |

Part Set-up – Coordinate System Set-up

Spatial Alignment

- Geometric axis is construction of the 2 Center points of the Upstream & Downstream Flanges (8” OD flanges), where the Upstream Flange has a tooling ball socket located in the –Y ordinate.

Planar Alignment

- Plane on Top Flange (+Y Flange)

“Z” Zero

- Mid-plane of the Upstream & Downstream Flanges

“X” & “Y” Zero

- Geometric axis of the 2 Upstream & Downstream Flanges, then shifted in –Y by a nominal distance of -0.850 (see drawing SA-391-264-03 R2)

| Upstream End View (-Z) | +X View |
| --- | --- |

Tooling Ball Measurements/Locations:

** Used 1” Offset Tooling Ball Adapter (1/2” sphere)

| Tooling Ball | FORM | Sph. Dia. | X | Y | Z |
| --- | --- | --- | --- | --- | --- |
| TB 1 | 0.0008 | 0.4952 | -0.0147 | -4.7224 | -2.9631 |
| TB 2 | 0.0022 | 0.4969 | 3.4912 | -2.7360 | -0.0504 |
| TB 3 | 0.0032 | 0.4963 | 3.4827 | 4.3977 | -3.4725 |
| TB 4 | 0.0008 | 0.4995 | 5.4891 | 4.3992 | 0.0240 |

** All tooling ball sockets (ID) fit fairly loose (wobble) with standard 1” offset Tooling Ball.

# Text boxes

+Y

Top Flange

Shift -0.850 in ‘Y’

+X

+Y

+Z

+X

TB1

TB2

TB3

TB4

+Y

+Z