SOMS B4C MASS ASSY

FIDUCIALIZATION REPORT

| Inspector: | Keith Caban |
| --- | --- |
| Customer: | MFD Vacuum Assembly |
| Date: | Friday, January 29, 2010 |
| Work Order/Charge No.: | 9242432 |
| Serial Number: | 001 |
| Drawing No: | SA-380-536-32 R0 |
| URL of Fiducial Report: | \\Web002\www-group\met\Quality\FIDUCIAL REPORTS\SOMS B4C MASK ASSY\SN-001.pdf |

Part Set-up – Coordinate System Set-up

Planar Alignment

| Mid-Plane of end Flanges Sets Zero in “Z” |  |
| --- | --- |

Spatial Alignment

| Mid-Plane of 2x Boron Carbide Shield Sets Zero in “Y” Mid-Point of 2x B4C Support Brackets Sets Zero in “X” |  |
| --- | --- |

Position of ID of Flange to B4C Coordinate System

X: +0.00631

Y: -0.00504

Tooling Ball Measurements/Locations

Projected cylindrical axis into 1” offset plane of the TB Adapter

| Tooling Ball | Form | Diameter | X | Y | Z | Perpendicularity |
| --- | --- | --- | --- | --- | --- | --- |
| TB 1 | 0.00069 | 0.25021 | 0.01100 | 4.85142 | 0.82847 | 0.00046 |
| TB 2 | 0.00062 | 0.25010 | -4.84941 | -0.01489 | 0.82518 | 0.00013 |

# Text boxes

+Y

+X

+Z

+Y

-X