SSRL SPEAR3 VERITICAL

SCRAPER FIDUCIALS

Inspector:  Keith Caban

Date:         September 17, 2004

Drawing #:SA-444-339-51

Charge #:  95-2702-0

Fiducial Coordinate System Set Up:

Vertical Scraper:

- R 6.00’s cylindrical axis  is the Z direction

  - This sets the Z Axis as the Spatial Alignment

  - +Z points towards Tooling Ball “V(2)”

- The Center point of the R 6.00 cylinder.

  - This sets zero in Y , with +Y going towards the R 6.000.

- The O.D. of Flange sets Zero in X, Z.

- Axis is created by the Symmetry Points of 2 holes in line with the leak check grooves.

  - This is the planar alignment for X direction  where +X is Tooling Ball “V(3)”

*Used ½” Tooling Balls with 1” extensions.

NON FIDUCIAL DATA:

| FEATURE | ACTUAL | NOMINAL | ACT – NOM |
| --- | --- | --- | --- |
| RADIUS 6.00 | 5.94802 | 6.00 | -.05198 |
| ANGLE of Cylindrical Axis to the X Axis | 90.00899 | 90 | 0.00899 |

FIDUCIAL DATA:

| TB | FORM | DIA | X | Y | Z |
| --- | --- | --- | --- | --- | --- |
| V1 | 0.00024 | 0.49573 | -2.21032 | -1.09421 | 0.00234 |
| V2 | 0.00011 | 0.49884 | -0.00223 | -1.13870 | 2.16920 |
| V3 | 0.00017 | 0.49839 | 2.15608 | -1.11729 | -0.03177 |
| V4 | 0.00054 | 0.49780 | -0.03968 | -1.10514 | -2.19534 |

# Text boxes

+Y

+Z

+Z

+X