# MFD NON-COMPLIANCE REPORT # 4479

Date: 02/26/03

Job #:

Sub ID:

Part Number: PF-451-017-95 R4

Part Description: FIXED MASK 3RD MACHINING (2 SIDES)

Engineer: JIM PECK

Ext: 4910

Reason For Non-compliance:

## SIDE 1

- Theoretical sharp corner distance 6.929 +.002/-.000 measures 6.92891 which is -.00009" out of tolerance

## SIDE 2

- Theoretical sharp corner distance 6.929 +.002/-.000 measures 6.92772 which is -.00128" out of tolerance

- Theoretical sharp corner distance 15.851 +.002/-.000 measures 15.85064 which is -.00036" out of tolerance

See inspection report