# MFD NON-COMPLIANCE REPORT # 4481

Date: 2/26/03

Job #: 16876

Sub ID:

Part Number: PF-290-310-02 Rev. 2

Part Description: Waveguide Base

Engineer: C. Rago

Ext: 3636

Reason For Non-compliance:

**** see profile plots****

2X - Basic distance 4.059  toleranced at a profile of 0.002 (± 0.001)

  - measures 4.0652 & 4.0644 on sn 001.

  - Measures 4.0613 & 4.0653 on sn 002.

See plot for Radii out of profiles.

Engineer has opted to use parts “as is”