# MFD NON-COMPLIANCE REPORT # 4487

Date: 2/28/03

Job #: 16986-3

Sub ID:

Part Number: PF-290-309-39 Rev. 2

Part Description: Waveguide Base (Jog Converter)

Engineer: C. Rago

Ext: 3636

Reason For Non-compliance:

Profile of 0.001 C-D (positive side in Y) is 0.001 to 0.009 out of tolerance

Profile of 0.001 C-D (negative side in Y) is 0.0015 to 0.004 out of tolerance

Profile of 0.001 A-B (positive side in Y) is 0.001 to 0.0065 out of tolerance

Profile of 0.001 A-B (negative side in Y) is 0.0006 to 0.0017 out of tolerance

Basic Dimension 1.442 ±0.001 is –0.0004 to –0.0017 out of tolerance on all parts except sn003

Basic Dimension 2.687 ±0.001 is –0.00017 to –0.0011 out of tolerance on parts sn001, sn002, sn007, sn008, and sn009 ONLY.

Parallelism of 0.002 from planar feature 1.435 (+z) to Datum –A- is 0.0027 out of parallel on part sn002 ONLY.

DO NOT USE SN002

Dry fit and measure 2X

See Inspection Report