# MFD NON-COMPLIANCE REPORT # 4492

Date: 3/4/03

Job #: 17056

Sub ID: 8

Part Number: PF-293-101-74

Part Description: Top Cover (Combiner Assy.)

Engineer: C. Rago

Ext: 3636

Reason For Non-compliance:

- Parallelism 0.001 of .126 planar surface to Datum –a-  is out of parallel by 0.0012”

- Slot profile of 0.001- position in x is off 0.0006”

- Profile of c----d

  - Is out of profile at R .125 (both sides) .0029”

  - Is out of profile at half distance of basic dimension 1.819 +.0009”

- Profile of a----b

  - Is out .0008” (bottom)

See profile plots attached

See inspection report

See Inspection Report

And attached profile/Flatness Plots

Test parts for fit per C. Rago.