# MFD NON-COMPLIANCE REPORT #5010

### Date:  4/17/03

Job #:  17088

Sub ID: 2

Part Number: PF-293-121-85 REV. 0

Part Description:  Assembly Machining (H-Plane Bend)

Engineer: C. RAGO

Ext: 3636

QTY: 4

Reason For Non-compliance:

ALL PARTS (SN 5001 – 5004) SEE PLOTS

- The inside aperture sn5001 on one side (1.435) = 1.420 poor form on cover side (~.013 form); same with sn5004; form of cover side = (~.004).  This is a datum, which throws off positional profile of outside profile |d|.001|A|B|C|, in which all sn's are to size, but throw off position due to datums having poor form.

- Form of inside aperture range from 0.002 to .013”

- SN 5004 has .0007 “bump” see plot Inside_prof(2).

Action Taken:

Engineer Signature: __________________________ Date:______