# MFD NON-COMPLIANCE REPORT #5000

Date:  3/17/03

Job #:  17047

Sub ID: 1

Part Number: PF-342-502-28 Rev. 0

Part Description: Waveguide Primary Machined

Engineer: M. Dormiani

Ext: 3129

Reason For Non-compliance:

SN002

- True Position Symetry distance 2X’s 3.543 of 0.002 to Datum Feature –A-  and Datum Feature –C- is out of position by 0.00654 and 0.00694.

- Surface of “ears” where Datum –c- is located on bottom surface, is not smooth, flatness is .007”.

SN004

- Diameter 3.425±0.004 is –0.0002” Out of Tolerance.

- True Position Symetry distance 2X’s 3.543 of 0.002 to Datum Feature –A-  and Datum Feature –C- is out of position by 0.01045 and 0.01084.

All Serial Numbers, Diameter 8.110 +0.000/ -0.001 are oversized between 0.0005 to 0.0010”

Action Taken:

Engineer Signature: __________________________ Date:______