# MFD NON-COMPLIANCE REPORT #5001

### Date:  3/17/03

Job #:  17047

Sub ID: 1

Part Number: PF-342-502-28 Rev. 0

Part Description: Waveguide Primary Machined

Engineer: M. Dormiani

Ext: 3129

Reason For Non-compliance:

BOTTOM PROFILES:

- Profile of Lid Rectangular cover is out of 0.001” profile by 0.0025” see plot (ACNO$LID)

TOP PROFILES:

- Profile of Curve line A-B is out of 0.001” surface profile by 0.0018” see plots [ACNO$AB(1) - Bottom, ACNO$AB(2) – Top]

- Profile of Curve line C-D is out of 0.001” surface profile by .0025” see plots [ACNO$CD(1) – Bottom, ACNO$CD(2) – Top]

  - Basic distance 3.842 of profile C-D is out of 0.001” surface profile by 0.0003” (undersized)

  - Slot profile (lid) is out  of 0.001” profile by 0.0031” (ACNO$SLOT_TOP)

  - Slot profile (small) is oversized by 0.007” (ACNO$SLOT_BOT)

## FRONT SIDE PROFILES:

- Inside Profile of Curve on the Right hand side is out of 0.001” surface profile by 0.0022”, see plots [ACNO$UPRT_IN(1), ACNO$UPRT_IN(2)].  (Left hand side is within tolerance.)

- Lid profile of curve on Right hand side is out of 0.001” profile by 0.0027”.  See plot (ACNO$UPRT_OUT)

- Inside profile of Curve (lower) is out of 0.001” surface profile by 0.0027”, see plots [ACNO$BOT_IN(1), ACNO$BOT_IN(2)]

- Lid profile of Curve (lower) is out of 0.001” surface profile by 0.0024”, see plots (ACNO$BOT_OUT)

Action Taken:

Engineer Signature: __________________________ Date:______