# MFD NON-COMPLIANCE REPORT #5019

### Date:  6/3/03

Job #:  12-1110-1

Sub ID:

Part Number: PF-767-171-01 Rev. 7 (Sketch)

Part Description:  Zero Length Male to Male Skarpaas Flange

Engineer: D. Palmer

Ext: 	4611

QTY: 1

Reason For Non-compliance:

- |j|.003|A|Cm|Dm| measured w/ 2X 0.3125 pins are out of position 0.0061” and 0.0075” (0.003” and 0.0045” Out of Positional Tolerance)

Action Taken:

Engineer Signature: _____________________ Date:______