# MFD NON-COMPLIANCE REPORT #5024

### Date:  7/9/03

Job #:  93-1211-4

Sub ID:

Part Number: PF-444-310-17 Rev. 1

Part Description:  RF Flange Machining

Engineer: N. Kurita

Ext: 	2850

QTY: 9

Reason For Non-compliance:

|j|.005|A|B|C| of Small Thru Slot is out of position measuring 0.0089” out of position on Serial Number: 19 ONLY.

|d|.001|A|D|E| of slot 6.444 × 2.786 measures 0.0015” on Serial Numbers: 38 and 39 ONLY.

SN 38 is missing 1x - #10-24 Threads, hole there, threads not.

All Other Dimensions are within specified tolerances.

Action Taken:

Engineer Signature: _____________________ Date:______