# MFD NON-COMPLIANCE REPORT #5025

### Date:  7/16/03

Job #:  93-1211-4

Sub ID:

Part Number: PF-444-310-47 Rev. 0

Part Description:  Girder Bellows RF Flange Machining

Engineer: N. Kurita

Ext: 	2850

QTY: 9

Reason For Non-compliance:

|j|.005|A|B|C| of Small Thru Slot is out of position by +.0038” on sn 18, +.0028 on sn 20, +.0014 on sn 41, +.0018 on sn 33, and +.0039 on sn 27.

|d|.001|A|D|E| of slot 7.658 × 2.426 is out of surface profile to the thru slot on all parts. +.0015” to +.0026” out of profile.

|j|n.002m|A|D|E| of diameter 0.2500 +0.0006”/-0.0000” is out of true position by 0.0026” on sn 01, .0019” on sn 18, .0017” on sn 20, .0019” on sn 27.

Distance 8.000 ± 0.005 is undersized on 7.9916 (-.0034” OT) on sn 28, and 7.9863  (-.0087” OT) on sn 27.

R 1.00 ± .01 is undersized on sn 28 0.9843 (-.0057” OT).

OT = out of tolerance

All Other Dimensions are within specified tolerances.

Action Taken:

Engineer Signature: _____________________ Date:______