# MFD NON-COMPLIANCE REPORT #5029

### Date:  9/16/03

Job #:  17525

Sub ID: 1

Part Number: PF-444-339-11 Rev 0

Part Description:  Transition, Octagon to 2.5” Dia.

Engineer: Andy Ringwall

Ext: 	8508

QTY: 1

Route part to: Customer

Reason For Non-compliance:

Diameter 2.500 ± 0.005 measures 2.506 (0.001” Out of Tolerance).

*****Customer, Please look at 2.1 transition depth, measures between 2.076 to 2.126.  Measures 2.103 @ rectangular intersections.

**** All other dimensions meet specifications. ****

Action Taken:

Engineer Signature: _____________________ Date:______