# MFD NON-COMPLIANCE REPORT #5030

### Date:  9/16/03

Job #:  26-0017-7

Sub ID: 0

Part Number: LAT-DS-00681 REV. 7

Part Description:  Mounting Plate

Engineer: J. Tice/B.J. Bhatnagar

### Ext: 	3427

### QTY: 2

Route part to: Customer

Units = Metric

Reason For Non-compliance:

Both Parts

|c|.05| measures 0.0565 and 0.0518.

|41.45| basic dimension for holes n10.31 is undersized 41.2771 and 41.2442

On Angled #10-24 threads (4X), |j|0.025m|A|D|E| are out of position 0.254 or greater (both parts).

On NON-Angled #10-24 threads (8X), |j|0.025m|A|D|E| are out of position 0.350 or greater (both parts).

|j|0.025m|A|D|E| of # 6-32 threads are out of position ranging from 0.1939 to 0.2521.

On Part 1 only, #6-32 Threads are actually M3 × 0.5 metric threads

On Part 1 only, vn 23 ± 0.8 measures 15.1789, which is made to Rev. 5

On Part 2 only, vn 6.35 +0.127/-0.000 are undersized 6.3380

Action Taken:

Engineer Signature: _____________________ Date:_________