# MFD NON-COMPLIANCE REPORT #5035

### Date:  10/23/03

Job #:  17662

Sub ID: -

Part Number: PF-293-121-91 Rev. 01

Part Description:  Rect to Rect Base

Engineer: J. Chan

### Ext: 	5084

### QTY: 5

Route part to: PRECISION

Reason For Non-compliance:

- The Inside profile is undersized, see plots.  Basic Dimension 1.204 ± 0.001” is undersized approximately 0.0016” on all parts as well as basic dimension 1.442 ± 0.001 is undersized the same.

- Lid Profile is large, SEE PLOT, however the lid fits.

- R. 0.005 ± 0.001 measures .0070” which is +0.0010” O.T.

- R 0.012 ± 0.001 measures 0.016” (+0.003” O.T.)

  - (R on mating part are reversed) see Lid measurement/ncr).

Action Taken:

Engineer Signature: _____________________ Date:_________