# MFD NON-COMPLIANCE REPORT #5035A

### Date:  1/27/03

Job #:  17952

Sub ID: -3

Part Number: PF-293-121-91 Rev. 01

Part Description:  Rect to Rect Base

Engineer: J. Chan

### Ext: 	5084

### QTY: 5

Route part to: PRECISION

Reason For Non-compliance:

- |d|.001|A|B|C| of machined mating lid profile is over sized on 2 parts

  - SN 1006 & 1007 (MADE BY BAY TECH.)

- See Photos for SN 1006, simulated match up cover to base does not seat well on SN 1006.

Action Taken:

Engineer Signature: _____________________ Date:_________