# MFD NON-COMPLIANCE REPORT #5041

### Date:  12/15/03

Job #:  17597

Sub ID: -17

Part Number: PF-293-121-89 REV 1

Part Description:  Oval to Rect. WG

Engineer: J. Chan

### Ext: 	5084

### QTY: 9

Batch 1

Reason For Non-compliance:

|d|.001|A|B|  Small Rectangle side, is out of surface profile ranging from +0.0001” to +0008”.  Size is good.  On serial numbers : 10003, 10004, 10005, 10006, 10007, 10008, 10009, 10010.

|d|.001|A|B|C| of the Inner Rectangle to Oval surface profile is out +0.0004” to  +0.0001” on parts 10002, 10003, 10008.

R 0.016 ± 0.001” is more shaped like a Chamfer than a radius.

Action Taken:

Engineer Signature: _____________________ Date:_________