# MFD NON-COMPLIANCE REPORT #5044

### Date:  01/15/04

Job #:  17956

Sub ID: 24

Part Number: SA-293-101-01 Rev. 01

Part Description:  Height Taper Assy. Machining

Engineer: J. Chan

### Ext: 	5084

Reason For Non-compliance:

- |d|.001|D|E|F| is out of surface profile by 0.0025” (See Plot ACNO$LG_CRV).

  - Further investigation, shows that the bottom Datum –D- surface used to create the coordinate system is not perfectly flat (0.004” Flat, see Plot DAT$PLA_D(1)).   Size is good, location is off in the +Y Direction.

- R .016 ± 0.001 measures 0.0120” (-0.003” undersized)

Action Taken:

Engineer Signature: _____________________ Date:_________