# MFD NON-COMPLIANCE REPORT # 5087

| PART NAME: | LOAD MOUNT RING | DATE: | 4/23/04 |
| --- | --- | --- | --- |
| PF/SA NO.: | PF-341-342-32 REV. 1 | INSPECTOR: | K. CABAN |
| WORK ORDER NO.: | 17784-27/20 | ENGINEER: | A. OWENS | EXT.: | 3168 |
| VENDOR | PACIFIC PRECISION MACHINE INC. | ROUTE TO: | PRECISION ASSY. |

| Reason For Non-Compliance: | Action (UAI,RWK,SCRP) |
| --- | --- |
| ¦d¦.004¦A¦B¦C¦ EXCEEDS SURFACE PROFILE REQUIREMENTS ON BOTH PARTS. 1 PART 0.0115, THE OTHER 0.0077. SEE ATTACHED PROFILE PLOTS, OUT OF PROFILE OCCURS IN SAME SPOT ON BOTH PARTS NEAR THE LOWER LEFT HAND CORNER WHERE THERE ARE TOOLING MARKS. | 1. |

| Engineer Signature: |  | Date: |  |
| --- | --- | --- | --- |