# MFD NON-COMPLIANCE REPORT # 5091

| PART NAME: | FRONT PLATE | DATE: | 5/7/04 |
| --- | --- | --- | --- |
| PF/SA NO.: | LAT-DS-03435 REV. 1 | INSPECTOR: | K. CABAN |
| WORK ORDER NO.: | 18561-2/20 | ENGINEER: | B.J. | EXT.: | 3427 |
| VENDOR | MFD LIGHTMS | ROUTE TO: | LIGHTMS |

| Reason For Non-Compliance: | Action (UAI,RWK,SCRP) |
| --- | --- |
| Distance 14.508 ± 0.002 is oversized out of tolerance by 0.0019 & 0.0024 on both parts. ¦j¦n.002¦A¦B¦C¦ of ¼-20 UNC 2A Threaded Holes are out of true position on all holes on both parts ranging from +0.0004 to +0.0095. ¦j¦n.001¦A¦B¦C¦ OF n.250-n.252 is out of true position on all holes on both parts ranging from +0.0019 to +0.0082. Depth of .50 on the .250 holes ±0.032 measure > .800. | 1. 2. 3. 4. |

| Engineer Signature: |  | Date: |  |
| --- | --- | --- | --- |