# MFD NON-COMPLIANCE REPORT # 5104

| PART NAME: | GRID SIMULATION PLATE | DATE: | 7/1/04 |
| --- | --- | --- | --- |
| PF/SA NO.: | LAT-DS-03509-01 | INSPECTOR: | K. CABAN |
| WORK ORDER NO.: | 26-0017-7 | ENGINEER: | J. TICE | EXT.: |  |
| VENDOR | DIAMOND TOOL & DIE INC. | ROUTE TO: | J. TICE |

| Reason For Non-Compliance: | Action (UAI,RWK,SCRP) |
| --- | --- |
| ¦d¦.006¦A¦B¦C¦ ¦d¦.0015¦A¦ is acceptable in Form, Location to datums, and Orientation, but according to Detail G, there is a unilateral tolerance for the basic dimensions on the bigger side. The ACTUAL measurement found that the basic dimensions were as much as -0.0023 smaller than nominal. *note part has been black oxidized and this condition could cause this non-conformance. | 1. |

| Engineer Signature: |  | Date: |  |
| --- | --- | --- | --- |