# MFD NON-COMPLIANCE REPORT # 5113

| PART NAME: | DOUBLE CORNER MNT BRACKET | DATE: | 8/27/04 |
| --- | --- | --- | --- |
| PF/SA NO.: | LAT-DS-03961 Rev. 1 | INSPECTOR: | K. CABAN |
| WORK ORDER NO.: | 26-0017-7 | ENGINEER: | NORDBY | EXT.: |  |
| VENDOR | NOT SPECIFIED | ROUTE TO: | GLAST/JEFF TICE |

| Reason For Non-Compliance: | Action (UAI,RWK,SCRP) |
| --- | --- |
| Distance 16.00 +0.0/-0.3 was oversized by 0.0795 on sn 1 and 0.0319 on sn 2. Distance (bottom side) 16.00 +0.2/-0.0 was oversized by 0.0080 on sn 1 and 0.0107 on sn 2. Distance (bottom side) 18.00 +0.2/-0.0 was oversized by 0.0211 on sn 1 and 0.0151 on sn 2. 0.2 MAX Protrusion of PEM NUT was oversized ranging from 0.300 to 0.045 on all parts and locations. |  |

| Engineer Signature: |  | Date: |  |
| --- | --- | --- | --- |