# MFD NON-COMPLIANCE REPORT # 5138

| PART NAME: | 2 CAM PLATE | DATE: | 8/17/05 |
| --- | --- | --- | --- |
| PF/SA NO.: | PF-380-712-05 R0 | INSPECTOR: | K. CABAN |
| WORK ORDER NO.: | 20214-29 | ENGINEER: | S. JANSSON | EXT.: | 5392 |
| VENDOR | MFD CENTRAL LAB | ROUTE TO: | CUSTOMER |

| Reason For Non-Compliance: | Action (UAI,RWK,SCRP) |
| --- | --- |
| Distance 3.260 +0.002/-0.000 was oversized by +0.0032” (3.2652) ¦j¦n.005¦A¦D¦C¦ of 5/16-18 UNC-2B were out of true position ranging from 0.0021 to 0.0026 on 2 of 8 holes. ¦j¦n.005¦A¦B¦C¦ of 3/8-16 UNC-2B were out of true position ranging from 0.0002 to 0.0049 on 5 of 8 holes. |  |

| Engineer Signature: |  | Date: |  |
| --- | --- | --- | --- |