# MFD NON-COMPLIANCE REPORT # 5159

| PART NAME: | LOAD CLOSURE PLATE | DATE: | 4/14/04 |
| --- | --- | --- | --- |
| PF/SA NO.: | PF-341-342-52 REV. 1 | INSPECTOR: | K. CABAN |
| WORK ORDER NO.: | 17784-43/40 | ENGINEER: |  | EXT.: | 3168 |
| VENDOR | PACIFIC PRECISION MACHINE INC. | ROUTE TO: | PRECISION |

| Reason For Non-Compliance: | Action (UAI,RWK,SCRP) |
| --- | --- |
| ¦c¦.002¦ MEASURES 0.0042 – 0.0047 ON BOTH PARTS. SEE ATTACHED PROFILE PLOTS. 9.498 +0.000/-0.002 is oversized on 1 part measuring 9.5003 12.998 +0.000/-0.002 is oversized on 1 part measuring 12.9985 0.25 ± 0.010 is oversized on 1 part measuring 0.262 |  |

| Engineer Signature: |  | Date: |  |
| --- | --- | --- | --- |