# MFD NON-COMPLIANCE REPORT # 5186

| PART NAME: | COUPLER FLANGE ASSY | DATE: | 05/18/06 |
| --- | --- | --- | --- |
| PF/SA NO.: | PF-341-341-31 REV 5 | INSPECTOR: | K. CABAN |
| WORK ORDER NO.: | 20294-20 | ENGINEER: | A. HILL | EXT.: | 4453 |
| VENDOR | THERMIONICS | ROUTE TO: | VAC ASSY |

| Reason For Non-Compliance: | Action (UAI,RWK,SCRP) |
| --- | --- |
| ¦d¦.004¦A¦B¦C¦ of ¦19.312¦ X ¦12.312¦ is out of surface profile on 5 of 6 parts. Range of profiles out of tolerance: 0.0050 to 0.0083. |  |

| Engineer Signature: |  | Date: |  |
| --- | --- | --- | --- |