# MFD NON-COMPLIANCE REPORT # 6000

Date:  3/12/03

Job #:  17173

Sub ID:  3

Part Number:  PF-444-416-28

Part Description:  Support Bracket

Engineer: T.A. Trautwein

Ext:  4753

Reason For Non-compliance:

Angle of 30 degrees +/- .5 degrees is 25.3 – 25.5  -- 3 of 3 parts

.50 +/- .010 is .514 - .516  -- 3 of 3 parts

1-8 thread gage will not enter – 1 of 3 parts (#2)