# MFD NON-COMPLIANCE REPORT # 6042

Date: 12/3/03

Job #:  17461, 5

Part Number: pf-342-981-08

## Part Description:  Shield Flange

Engineer:   S. DeBarger, x4647

Reason For Non-compliance:

- ¼-20 hole pattern is oriented using the wrong view.  As a result, the clocking of the    pattern is out of location by approximately 50°.

- Parts have chatter marks as well as burrs.

- .62 MAX is  .685 - .700

- .404 +/-.002 is .409 – 1 piece only

- R .127 +.005/-.000 is <= .122 on 2 of 4 pieces.

- Note 3 has been violated, there is no part number on parts

Action Taken:

Note 1 has been resolved.  New holes machined.  Previous holes still exist and are acceptable per S. DeBarger.

Remaining problems still need to be resolved.

Engineer Signature: __________________________